## Slide 1: HW–SW Co‑Design Project
Roy Dayan
Dor Knafo

## Slide 2
Deep Copy Benchmark

## Slide 3: Overview
deepcopy python library creates a full, independent copy of complex objects (unlike shallow copy).
Goal: identify bottlenecks and optimize execution efficiency.
Tools: CPython 3.10.12 pyperformance Linux perf flame graphs

## Slide 4: How Python Works
Cpython

## Slide 5: Initial Analysis
Baseline deepcopy profiling performed on CPython 3.10.12 using pyperformance and flame graphs.

## Slide 7: Initial Analysis
Most CPU time spent in the interpreter loop (PyEval_EvalFrameDefault).
Conclusion: execution time may be dominated by interpreter overhead rather than raw data movement - leading us to explore C-level optimization as the next step.

## Slide 8: Baseline Benchmark Results

## Slide 9: Optimizations
Implemented a native C extension module named fastcopy.c.
Added C implementations for lists, dicts, and tuples deep copy routines.
Modified copy.py to call these C functions directly when available.
This bypassed Python bytecode loops and reduced interpreter overhead.
Result: fewer function calls, better cache locality, and faster execution.

## Slide 10: Example: C-based Optimization deepcopy_list_c

## Slide 11
fastcopy.c

## Slide 12
copy.py

## Slide 13: Correctness Verification
Verified deepcopy correctness after optimization.
Tested nested, composite, and self-referential structures.
Ensured copies are independent and structurally identical.

## Slide 14: Optimized Benchmark Results

## Slide 16: Performance Comparison
6.24% speedup (845.3 → 792.5 µs).
Executed ~14% fewer instructions, indicating lower CPU workload.
The performance gain mainly results from reduced interpreter loops.
Cache-miss and branch-miss rates fluctuated between runs, likely due to fewer memory accesses overall, making the relative ratios more sensitive to small variations and system noise.

## Slide 18: Hardware Acceleration Proposal
FastCopy Hardware Accelerator (FCA)
Offloads recursive deep copy operations from software to hardware.
Uses DMA and descriptor-based traversal for parallel memory copying.
Benefits: lower latency, reduced CPU load, and higher throughput.
Trade-offs: added hardware complexity and power consumption.

## Slide 19: FCA Block Diagram

## Slide 20: Conclusion
C-level optimization reduced deepcopy runtime by ~5.8% and cut instruction count by ~14%.
Verified full functional correctness - identical results with improved efficiency.
Proposed hardware accelerator could further enhance performance for large datasets.
Demonstrates how profiling-driven HW–SW co-design effectively removes bottlenecks and boosts execution speed.

## Slide 21
Json Dumps Benchmark

## Slide 22: Overview
json.dumps converts Python objects to JSON-formatted strings

## Slide 23: Overview
pyperformance json_dumps repeats serialization of nested objects
Workflow:
  profile  identify bottlenecks  optimize  re‑measure
Preliminary result: stdlib json = 62.2 ms ± 0.5 ms

## Slide 24: Initial Analysis
Ran microbenchmark with stdlib json
Generated flame graph:
Bottlenecks?

## Slide 25: Initial Analysis
Stdlib json already has native C speedups!
Without C speedups:
With C speedups:

## Slide 26: Initial Analysis
Note the python stack is “deep”
pyperformance main loop:
  dumps calls JSONEncoder::encode which calls iterencode
  Lots of conditionals and eventually calls C functions to encode
  Program spends long time in python  seek to minimize

## Slide 27: Optimization – Substitute orjson
High-performance JSON library
Native Rust implementation
  Avoids slow Python conditionals and interpreter overhead
  Utilizes SIMD to process multiple characters in parallel
Result: stdlib json = 62.2 ms ± 0.5 ms; orjson = 11.9 ms ± 0.1 ms

## Slide 28: Integration - routing calls to orjson
“Monkey‑patch” json.dumps → orjson.dumps
  Create sitecustomize.py and put in PYTHONPATH folder (env variable)
  Run benchmark with flag for pyperformance processes to see patch
# Monkey‑patch json.dumps to use orjson.dumps PATCHDIR=$(mktemp -d) cat > "$PATCHDIR/sitecustomize.py" <<'PY' import json try: import orjson json.dumps = lambda obj, *a, **kw: orjson.dumps(obj).decode("utf-8") except Exception as e: import sys print("[sitecustomize] orjson patch failed:", e, file=sys.stderr) PY export PYTHONPATH="$PATCHDIR"
# Run benchmark with flag python3-dbg -m pyperformance run --bench json_dumps --inherit-environ=PYTHONPATH

## Slide 29: Optimized Analysis — orjson
Flame graph on same microbenchmark:
Shallow native stack
Interpreter frames largely gone

## Slide 30: Runtime – pyperformance
Variant | Mean ± stdev (ms) | Δ vs. baseline
stdlib json.dumps | 62.2 ± 0.5 | —
orjson (patched) | 11.9 ± 0.1 | −80.9% (~5.24×)

## Slide 31: HW counters – perf stat
Note: stats from full pyperformance program
Metric | stdlib | orjson | Change
instructions | 167,287,865,175 | 96,822,927,687 | −42.1%
branches | 35,540,658,013 | 20,984,549,290 | −41.0%
branch misses | 335,263,393 | 156,514,197 | −53.3%
cache misses (% of total accesses) | 17,259,734 (2.64%) | 6,968,728 (2.15%) | −59.6%
IPC | 1.83 | 1.93 | +5.5%
Elapsed (s) | 39.91 | 20.30 | −49.1%

## Slide 32: Hardware Acceleration Proposal
JSON Encode Accelerator (JEA)
Motivation:
  Heavy encoding (UTF-8), number→text formatting, special char handling
  Aim: offload to HW
Implementation:
  SW iterates over Python object with simple prepare_tokens()
    Stores ‘token’ stream + string lookup table in memory
    Tokens are coded components of the object
    Table translates IDs individual strings
  HW accesses stream + table to encode JSON string and writes into buffer
    Treats tokens as its ISA!

## Slide 33: Token Generation
Object: {"a": 1, "ab": [2, "x"]}
Token Stream: OBJ_BEGIN
KEY( id=0 ) # "a"
VAL_INT(1)
KEY( id=1 ) # "ab"
ARR_BEGIN
VAL_INT(2)
VAL_STRING(id=2) # "x"
ARR_END
OBJ_END
Table: 0 – “a”, 1-“ab”, 2-“x”

## Slide 34: HW-SW Interface
Inputs: token stream, lookup table, doorbells, options
Outputs: contiguous JSON-formatted string, completion element
Requirement:
  Edit orjson library: prepare_tokens(obj) -> (tokens, str_table)
  Enable doorbells thru driver
  Enable JEA DMA-read tokens+table, write into provided buffer
  Completion + SW poll&read  return JSON-formatted string

## Slide 35: JEA Block Diagram

## Slide 36: JEA Performance Analysis
Amdahl’s law:
  Estimated time spent in JSON formatting: 70% (from flame graphs)
  Neglect added latencies (DMA, doorbells, completion post+polling)
  Speedup determined by concurrent characters processed
    Assume 4x orjson SIMD limitation
  That is, ~2x acceleration over orjson  ~10x over stdlib json!

## Slide 37: JEA Area/Power Trade-offs
Area:
  Character formatting logic (small)
  DMA unit, caches (scale with performance gains)
    More parallelism  better performance, larger inputs and caches
  Niche unit (though can be adapted for other vectorized operations)
Power
  Efficient per-character encoding
  SRAMs for stream, table fetching and reorder buffers

## Slide 38: Conclusion
orjson delivers 5× speedup over stdlib
  Eliminates python stack and interpreter overhead
  Utilizes SIMD capabilities for parallel string processing
  Perf counters confirm efficiency
JEA provides additional 2× speedup by offloading heavy encoding
HW-SW co‑design produces substantial gains 